bds Example: Three generators are scheduled to supply the system load. The unit 1 has the startup cost of 100$ and generation cost of 8$/MWh, with generation capacity from 5MW to 100MW. The unit 2 has the startup cost of 120$ and generation cost of 10$/WMh, with generation capacity form 5MW to 20MW. The unit 3 has startup cost of $180 and generation cost of 12$/MWh, with generation capacity form 5MW to 20M. The initial status of all units is off, and can be turned on if needed. Ramping up/down, minimum ON/OFF and other constraints are ignored for simplicity. The Unit 2 and 3 can be quickly committed right after uncertainty is disclosed, to cover the system load. The quick-start-capability of unit 2 and 3 are 15 MW. Find the optimal commitment decision for the two-hour ahead unit commitment problem,

Table 1 Load forecast for individual scenario (MW)

| Scenario | Probability | T=1 | T=2 |
| --- | --- | --- | --- |
| 1 | 0.5 | 90 | 110 |
| 2 | 0.5 | 95 | 100 |

The whole problem is formulated as

Subject to startup and shutdown indicator constraints:

Power generation limits for unit 1

Power generation limits for unit 2, where  represents quick-start commitment decision of unit 2 at time t after uncertainty scenario  is disclosed.  is equal to 1 if unit 2 is not committed in the first-stage but committed in scenario , otherwise 0.

Startup cost of unit 2 at scenario

.

Similar power generation limits and startup cost for unit 3

Power balance constraints

The problem is solved by the extended L-shaped method results are shown in Table 2

Table 2 Optimal solution

| Scenario |  | Commitment | Dispatch (MW) |
| --- | --- | --- | --- |
|  |  | T=1 | T=2 | T=1 | T=2 |
| 1 | Unit 1 | 1 | 1 | 90 | 100 |
|  | Unit 2 | 0 | 1 | 0 | 10 |
|  | Unit 3 | 0 | 0 | 0 | 0 |
| 2 | Unit 1 | 1 | 1 | 95 | 100 |
|  | Unit 2 | 0 | 0 | 0 | 0 |
|  | Unit 3 | 0 | 0 | 0 | 0 |